## Slide 1: Oval
#1 Turn on Partworks v2

## Slide 2: PartWorks v2

## Slide 3: OR turn on Aspire

## Slide 4: Create New file “Click”

## Slide 5: Create New File (Aspire)

## Slide 6: Input
Size
      X –dimension- 16 Width
      Y- dimension - 10 Length
Material
      _ Z – dimension - .75 Thickness
Origin
    Click xy origin Bottom left
Units
      Select INCHS
      Click OK

## Slide 7: PartsWorks New Under- Create Vector Choose “Draw Elipse” Click

## Slide 8: Under Create Vectors
Draw oval using icon

## Slide 9: Drawing
Choose anchor point
Size
  Width 8
  Height 4.5
Hit Create button
Draw Elipse

## Slide 10: Click Close Button

## Slide 11: Pick top left icon

## Slide 12: Highlight your rectangle by clicking one line it will turn Pink

## Slide 13: Align
Align Objects:
    “Click” White centering material button
      Material oval will center on block
      On screen right move cursor to (yellow) TOOLPATH

## Slide 14: Toolpath box Under:” Toolpath operations” Select “Create profile toolpath” “Click “

## Slide 15: 2D Profile Toolpath

## Slide 16: Calculations
1- Enter Start Depth 0 inchs
2- Enter Cut Depth .75
3- Under Tool selection “click”
Select

## Slide 17: Tool Database

## Slide 18: Tool Database
Under Tool list
  Scroll down find Sb starter set
  “click” on Upcut bit ¼”
  Bottom right of screen “click” on OK

## Slide 19: 2D profile Toolpath w/bit selection

## Slide 20: Machine Vectors
1- Select Outside /right “click”
2- Select Conventional “click”
3 -Select Tabs Add Tabs “click”

## Slide 21: Tabs

## Slide 22: Tabs
1- Under length .65 inchs
2- Under thickness .185 inchs
3- Check √ 3d tabs
4- Select Edit tabs button “click”

## Slide 23: Toolpath Tabs

## Slide 24: Toolpath Tabs
Add tabs
    Select constant distance between tabs “click”
    Distance: 6”
      Minimum # 4
      Maximum # 4
        “click” on ADD TABS button

## Slide 25: Tabs Toolpath

## Slide 26: “Click” CLOSE button

## Slide 28: Under name put “Your Name”
Click Calculate button

## Slide 29: Calculated path
Now “Click” Close!
Find pre-view mode

## Slide 30: ToolPath
Now Click pre-view toolpath

## Slide 31: Toolpath w/tabs
Click on Close button

## Slide 32: Toolpath summary
Click on Save Toolpath icon

## Slide 33: Save
Click on the Save Toolpath Icon

## Slide 34: Select “Your Name” toolpath
Check box √ your name

## Slide 35: Click Save Toolpath button
Do it!

## Slide 36: Save in SbParts File name: Your name Click Save button

## Slide 37: Next
Bottom right on Toolpaths
  Click the CLOSE button:

## Slide 38: 3D view

## Slide 39: Next:
Click on File (top left of screen)
Go To: SAVE AS Click

## Slide 40: SAVE AS box

## Slide 41: SbParts
Under Sbparts
Type your name to file name
“Click” Save Button
Now minimize program
“Click” on Shopbot 3 Icon

## Slide 42: Shopbbot 3

## Slide 43: Box Control
Click “ Continue in Preview Mode.
Click “ on OK button.

## Slide 44: Shopbot Console

## Slide 45: Load Profile Click on Green Load Profile button
Your file
Load Part

## Slide 46: Select Shopbot Part file
Look in SbParts
Find your name file
Select:
“Click” OPEN

## Slide 47: Fill in Sheet

## Slide 48
Click Green Start button:

## Slide 49: Shopbot Preview

## Slide 50: Continue on Preview mode
Shopbot continue pre-view
“click” OK
If rpm box open click x and close.

## Slide 51: Successful preview

## Slide 52: Success
If preview ran successfully
Run preview past instructor for OK!
Then Follow same instructions from shopbot 3 in MOVE/CUT mode on shopbot position bar

## Slide 53: Prepare your position
Clamp your piece down on table
  With vacuum system
  Screws in corners (away from bit)
  Manual clamps (away from bit)
Find center of your piece with router bit by moving the router with the.

## Slide 54: Shop bot keypad

## Slide 55: Move to center point
Move with keypad
First raise your z axis so you do not hurt bit
Next move X & Y till centered over your work piece
Zero out x & y at this point
Next zero the Z axis

## Slide 56: Setting up for z axis
Put your clip on router bit
Set the z plate on your workpiece
Directly under the bit

## Slide 57: Click on the left red arrow icon

## Slide 58: After
Remove the clip
Replace the plate to storage place
Click ok

## Slide 59: Move/Cut

## Slide 60: Turn on Router
Remember to turn on router when asked

## Slide 61: Read! Start router with green start button!

## Slide 62: Run file
Of coarse make sure the dust collector is on
Make sure the vacuum system is on
Make sure the piece is in correct starting position.

## Slide 63: Go to SbParts
Look up your name and open file.
GOOD JOB!